## Slide 1: 基于原地卷积网络的前端信号处理算法
张学良
(合作者：刘晋江，张成刚）
内蒙古大学，计算机学院
语音信号处理组

## Slide 2: 提纲
背景
原地卷积网络 inplace convolutional recurrent network
基于原地卷积网络的多通道语音增强
基于原地卷积网络的声学回声消除
基于原地卷积网络的混响消除 dense recurrent convolutional network
总结

## Slide 3: 背景
背景噪声
干扰人声
房间混响
设备播放的声音
噪声抑制
混响消除
声学回声消除
语音通讯
自动语音识别
助听器设计

## Slide 4: 背景
麦克风信号
  其中，麦克风信号，目标语音，噪声向量，扬声器播放信号(参考信号），目标语
  音导向矢量，目标语音混响传播路径，回声传播路径。
前端信号处理
  其中，麦克风信号和参考信号到目标语音的映射

## Slide 5: 传统信号处理 VS 深度学习
 | 传统信号处理 | 深度学习
单通道降噪 | 维纳滤波 | CRN[1] + 单mic输入
多通道降噪 | MVDR | CRN[2] + 多mic输入
声学回声消除 | LMS | CRN[3] + mic和ref输入
混响消除 | WPE | CRN[4] + 单/多mic输入
[1] Tan K. and Wang D.L. (2018): A convolutional recurrent neural network for real-time speech enhancement. Proceedings of INTERSPEECH-18, pp. 3229-3233.
[2] Tan K., Wang Z.-Q., and Wang D.L. (2022): Neural spectrospatial filtering. IEEE/ACM Transactions on Audio, Speech, and Language Processing, vol. 30, pp. 605-621.
[3] Zhang H., Tan K., and Wang D.L. (2019): Deep learning for joint acoustic echo and noise cancellation with nonlinear distortions. Proceedings of INTERSPEECH-19, pp. 4255-4259.
[4] Wang Z.-Q. and Wang D.L. (2020): Multi-microphone complex spectral mapping for speech dereverberation. Proceedings of ICASSP-20, pp. 486-490.
深度学习：大数据量+大模型
  泛化性问题
  模型复杂度高
*CRN：Convolutional Recurrent Network

## Slide 6: CRN
Encoder（多层卷积）+ LSTM + Decoder（多层反卷积）
全频带建模
Gated CRN、Dense CRN等
Frequency dimension

## Slide 7: 原地卷积网络
卷积层不做降采样
反卷积层不做升采样
采用channel-wise LSTM，每个频点的特征单独输入LSTM中
所有频点共享一个LSTM
（以此实现频带间的独立处理）
采用复数谱作为整个网络输入
同时预测网络幅度和相位

## Slide 8: 基于原地卷积网络的多通道语音增强
Speech：
  AISHELL-1 (Mandarin): Training(29 hours), Validation(1 hour)
  TIMIT : Test
Noise:
  NOISEX92: Test (destroyerops, white, and babble) Train(rest 12 type of noises)
Location： IMAGE method
  9 for training with 22.5◦ interval
  17 for test with 11.25◦ interval.
Microphones:
  Room center with 2cm interval
Evaluation metrics:
  Short-time objective intelligibility (STOI)
  Perceptual evaluation of speech quality (PESQ)
  Signal-to-distortion ratios (SDR)
Jinjiang Liu and Xueliang Zhang, “Inplace Gated Convolutional Recurrent Neural Network for Dual-Channel Speech Enhancement,” in Proc. Interspeech 2021, pp. 1852–1856.

## Slide 9: 结果
* MVDR的结果基于真实方向

## Slide 10
mixture
clean
IGCRN
GCRN
MVDR
Notes: 4nd, we test how the downsampling influnce the perfermance, as we can see when the downsampling time increase the performance gradually decay.

## Slide 11: 基于原地卷积的声学回声消除
Training
  200 pairs of speakers fromTIMIT corpus which contains 630 speakers
  rooms of size l × w × h, l [4m,10m] , w [5m,11m] , h [3m,4m].
  distance between mic and loudspeaker [0.5, 0.7, 0.9]m.
  T60 [0.2, 0.3, 0.4, 0.5, 0.6]s, 10,000 RIRs are created.
  SER randomly chosen from [-9, -6, -3, 0, 3, 6, 9] dB.
  30,000 mixtures for training and 2,000 for validation.
Test
  Testing room = [4, 5, 3]m, T60=0.35s. distance 0.6 m.
  Choose unseen 100 pairs of speakers for testing.
Evaluation Metric
  ERLE: 度量回声残余
  PESQ: 近端信号保真度

## Slide 12
结果
Chenggang Zhang, Jinjiang Liu and Xueliang Zhang, “A Complex Spectral Mapping with Inplace Convolution Recurrent Neural Networks For Acoustic Echo Cancellation,” ICASSP 2022, pp: 751-755.

## Slide 13
DEMO https://chenggangzhang.github.io/ICRN-AEC
（a）Microphone signal
（b）Target signal
（c）ICRN
（d）WebRTC-AEC3
（e）BLSTM
（f）CRN

## Slide 14: 基于原地卷积的混响消除
DRC block
  增加了时间维度的建模
  频率维度: 双向 LSTM
  时间维度: 单向 LSTM（确保因果性）
DRC NET
  取消了原本CRN中的LSTM
  保留了升、降采样卷积（方便平衡算力和模型参数量）

## Slide 15
Speech corpus:
  WSJCAM0
Reverberation simulation:
  RIR generator (IMAGE method)
  reverberation time (T60): 0.2s - 1.3s
Noise:
  REVERB challenge noise
  [5, 25] dB SNR
Microphones:
  4-channel uniform circular mircrophone array
  20cm aperture
Room configurations:
  room length & width: [5,10]m
  room height: [3,4]m
Speech source:
  distence: [0.75, 2.5]m away from micropones
STFT:
  32 ms frame length,
  8 ms frame shift,
  hann window
  257-dimension complex spectrum
Evaluation metrics:
  Extended short-time objective intelligibility (ESTOI)
  Perceptual evaluation of speech quality (PESQ)
  Signal-to-distortion ratios (SDR)
Experiments
实验设置
Notes: This is the experimental setup.

## Slide 16: 结果
Jinjiang Liu, Xueliang Zhang, “DRC-NET: Densely Connected Recurrent Convolutional Neural Network for Speech Dereverberation,” ICASSP 2022, pp: 166-170.

## Slide 17
Tiny DRC-NET for laptop computer : 0.11G MAC 0.14M Param
Real Recording
Processed
Notes: This is the experimental setup.

## Slide 18: 总结
受传统信号处理算法的启发，我们提出了inplace convolution和channel-wise LSTM的处理方式，提出了频带独立模型。
模型可以较好地保留输入频点的位置信息，降低了学习难度。
该模型和其扩展模型用于多通道语音增强、回声消除、混响消除等任务，均有良好表现。同时，有效的降低了模型的参数量。

## Slide 19: 谢谢